## Slide 1
Pore-scale experimental measurement and interpretation of low carbon dioxide/brine relative permeability
Anfal AL Zarafi
Supervisors: Prof. Martin Blunt & Dr. Branko Bijeljic
14/01/2026

## Slide 2
Outline
Research Objectives
Challenges in Steady-State Relative Permeability Measurements and Previous Studies
Experimental Work
Results
Future Work
Conclusions

## Slide 3
Research Objectives
Improve understanding of CO₂ storage in porous media.
Study supercritical CO₂ flow and pore-scale relative permeability.
Develop a method for steady-state two-phase flow with micro-CT imaging.
Analyse pore-scale changes in occupancy, connectivity, and flow (Ostwald ripening).
Generate benchmark high quality data using outcrop samples.
Extend data collection to actual reservoir rocks (sandstone & carbonate).
Investigate relative permeability hysteresis.

## Slide 4
Challenges in Steady-State Relative Permeability Measurements
Experiments are time consuming and the measured relative permeability is affected by the non-uniformity in saturation profiles.
Manual or semi-automatic threshold selection can lead to inconsistent saturation segmentation, segmentation uncertainty can create variation in relative permeability, depending on pore occupancy assumptions (Krygier et al., 2020).
Heterogeneity in the sample cause uneven saturation distribution, challenging CT resolution and segmentation accuracy (Boon & Beson, 2021).
Laboratory samples may not fully replicate large-scale heterogeneity that largely impacts relative permeability thus we need models to bridge core-scale CT data to field-scale plume migration (Krevor et al., 2012).
Study | Rock | Condition °C/MPa | Method | Scale |  | 
(Botset, 1940) | Berea sandstone | - | SS | Core-scale | 0.61 | 0.87
(Bennion & Bachu, 2005) | Reservoir sandstone | 20°/3.4 | USS | Core-scale | 0.12 | 0.34
Perrin et al., (2009) | Berea sandstone | 20°/12.4 | SS | Core-scale | 0.10 | 0.44
Krevor et al., (2012) | Berea Sandstone | 50°/9 | SS | Core-Scale | 0.55 | 0.38
(Akbarabadi & Piri, 2013) | Berea & nugget sandstone | 55°/11 | ss | Core-Scale | 0.47 | 0.20
Reynolds & Krevor (2015) | Bentheimer sandstone | 42°/13.5 | SS | Core-Scale | 0.73 | 0.262
Chai et al. (2025) | Reservoir sandstone | 50°/8 | SS | Pore-Scale | 0.88 | 0.47
Study | Rock | Condition °C/MPa | Method | Scale |  | 
(Botset, 1940) | Berea sandstone | - | SS | Core-scale | 0.61 | 0.87
(Bennion & Bachu, 2005) | Reservoir sandstone | 20°/3.4 | USS | Core-scale | 0.12 | 0.34
Perrin et al., (2009) | Berea sandstone | 20°/12.4 | SS | Core-scale | 0.10 | 0.44
Krevor et al., (2012) | Berea Sandstone | 50°/9 | SS | Core-Scale | 0.55 | 0.38
(Akbarabadi & Piri, 2013) | Berea & nugget sandstone | 55°/11 | ss | Core-Scale | 0.47 | 0.20
Reynolds & Krevor (2015) | Bentheimer sandstone | 42°/13.5 | SS | Core-Scale | 0.73 | 0.262
Chai et al. (2025) | Reservoir sandstone | 50°/8 | SS | Pore-Scale | 0.88 | 0.47
Table: Experimental studies with CO2/brine flow in sandstone rock samples at different conditions and scales; ss: steady state, uss: unsteady state.

## Slide 5
Experimental Apparatus and Methodology
Bentheimer Sandstone (L: 20.59mm, D: 6.01mm).
Fluids include supercritical CO2 and brine doped with 25wt% KI.
Experiment conditions of 8 MPa pressure and 50ºC temperature.
Zeiss Xradia 510 Versa micro-CT was used for image acquisition.
Injecting at a total flow rate of 0.1 ml/min.

## Slide 6
Absolute Permeability and Porosity
Brine was injected at different flow rates, while pressure differential was monitored to determine the absolute permeability using Darcy’s law.
Porosity across the length of the sample was extracted from the dry X-ray image.
K = 1.3  0.1 D

## Slide 7
Image processing
Voxel size was 3.6 µm.
Normalized grey-values and non-local means filter.
Image segmentation was performed using a combination of differential imaging, interactive thresholding, and interactive top-hat filtering to distinguish the three phases: rock, brine, and CO2.
Zoomed-in images were acquired to study a region of interest (ROI) at 1.65 µm resolution.

## Slide 8
Image processing
Pore network extraction enabled the quantification of pore radius distribution.
Intermediate-sized pores dominate the pore space.
Spatial analysis of pore sizes indicates overall macroscopic homogeneity.
An increase in large pore frequency toward the top quarter of the sample.
Pore Network Analysis and Gas Occupancy

## Slide 9
Saturation Profile
CO2 saturation increased with an increase of its fractional flow from 0% at ƒg= 0 to 56.7% at ƒg= 1.
A rapid increase in saturation is prominent at the top of the sample corresponding to the presence of large pores observed in the pore network at the same location.
Inhomogeneous behaviour is corrected for to calculate relative permeability using methods previously developed in the group.

## Slide 10
Relative Permeability
To accommodate the impact of local inhomogeneous saturation profiles in the direction of the flow, a semi-analytical correction is made to relative permeability with an assessment of uncertainty.
As the saturation of CO2 increases, the relative permeability of brine decreases sharply.
Modest increase in the gas relative permeability (0.241 under 100% gas injection).

## Slide 11
Interfacial Curvature
The interfaces between gas and brine are extracted from the segmented images at ƒw=0.7.
Interfaces appear quasi-spherical, encapsulating the gas within the large pores.
most interfaces cases show two positive curvatures giving a positive Gaussian curvature.
Signature of a water-wet system in which the non-wetting phase (gas) can be trapped and retained in the pore space with a poor overall connectivity.

## Slide 12
CO2 Ganglia Evolution and Connectivity
Image segmentation was performed using a combination of differential imaging, interactive thresholding, and interactive top-hat filtering to distinguish the three phases: rock, brine, and CO2.
Configuration of CO2 ganglia at different fractional flows was extracted from the corresponding zoomed-in images.
In the early stages of drainage (ƒg=0.3 and 0.5), most of the CO2 ganglia appear small, disconnected and widely dispersed throughout the pore space of the sample.
The ganglia appear disconnected due to Roof-snap-off. Euler number almost always positive, indicating poor connectivity.
Fractional flow of gas | Euler number (1/mm)
0.1 | 0.24
0.3 | 14.80
0.5 | 9.94
0.8 | 2.67
0.95 | 14.31
1.0 | -7.03
Table: Normalized Euler characteristic at different fractional flows of gas

## Slide 13
Capillary Pressure
Capillary pressure estimated from interfacial curvatures.
Results show good agreement with results from porous plate method on the same rock type.
Capillary pressure remains positive and increases with the increase of gas saturation.

## Slide 14
Conclusions and Future Work
A pore-scale investigation combining steady-state relative permeability measurements with X-ray microtomography provides new insight into CO₂/brine drainage behaviour in strongly water-wet Bentheimer sandstone under reservoir conditions.
CO₂ relative permeability remains intrinsically low (endpoint ≈ 0.24), confirming limited gas mobility as a fundamental feature of the CO₂/brine system.
CO₂ invades larger pores preferentially, but snap-off driven by low gas viscosity limits phase connectivity and suppresses relative permeability.
Interfacial curvature indicates a strongly water-wet system, with curvature-derived capillary pressures increasing with gas saturation and matching porous-plate data.
The results offer a robust benchmark for pore-scale modelling and improve prediction of CO₂ storage performance in saline aquifers.
Upcoming experiment will examine relative permeability and gas connectivity in a reservoir sandstone sample. The results will be compared to this work.

## Slide 15
Thank You