## Slide 1
Machine Learning and NMR Interpretation for Porous Media
Gang Luo, Lizhi Xiao, Branko Bijeljic and Martin Blunt
24th Meeting of the Imperial College Consortium
on Pore-Scale Modelling and Imaging
16/01/2024
Department of Earth Science and Engineering, Imperial College London
College of Artificial Intelligence, China University of Petroleum
Imperial College
London

## Slide 2
Background
Methodology
A Lightweight Multiscale Neural Network (LMsNN) for
the Inversion of Relaxation Spectra
Experiment
Validation of Synthetic Data
  Application of NMR Rock Core Analysis
Processing with NMR Logging Data
Discussion and Further Work
Outline

## Slide 3
NMR Well Logging
Rock Core Analysis
Echo Signals
NMR Measurements
1-D Spectrum
2-D Spectrum
Inversion of the Spectra
Further Analysis
Pore-size
Distributions
Fluid Distributions
GeoSpec core analysers, Oxford Instruments
Porosity
Wettability
Capillary Pressure
Permeability
Background

## Slide 4
Strong Noise contained in signals.
Inversion is an underdetermined process (Multi-solution).
Challenges
Use Machine learning to reduce the noise in the echo signals.
Improving the accuracy of the inverse spectrum.
Research Motivations
Signals
T2 spectra
Noise
1.5
0
500
Times (ms)
Amplitude(p.u.)
CPMG Pulse Sequence Response Equation
Background

## Slide 5
Luo, Gang, Luo, Sihui, Xiao, Lizhi, Blunt, Martin J., Bijeljic, Branko, Liao, Guangzhi, and Rongbo Shao. "NMR Logging Data Processing Using Deep Learning." Paper presented at the SPWLA 64th Annual Logging Symposium, Lake Conroe, Texas, USA, June 2023. doi: https://doi.org/10.30632/SPWLA-2023-0026
My previous work: A Supervised Deep Learning Method for the Inversion of the T2 Spectra
The spectra with Gaussian distribution is considered as a priori knowledge to construct an NMR synthetic dataset.
The network perform signal denoising and relaxation spectrum inversion simultaneously.
The approach was validated on core analysis.
Background

## Slide 6
Luo, Gang, Luo, Sihui, Xiao, Lizhi, Blunt, Martin J., Bijeljic, Branko, Liao, Guangzhi, and Rongbo Shao. "NMR Logging Data Processing Using Deep Learning." Paper presented at the SPWLA 64th Annual Logging Symposium, Lake Conroe, Texas, USA, June 2023. doi: https://doi.org/10.30632/SPWLA-2023-0026
Inversion results using Bulter–Reeds–Dawsons (BRD) inversion for 256-scan echoes, and inversion results of BRD and ATT-CNN models for low SNR echoes. The noisy echoes and denoised echoes are compared to illustrate the denoising performance.
A Supervised Deep Learning Method Results
Background

## Slide 7
The supervised training approach highly dependent on the synthetic dataset. Constraints and assumptions may not be suitable when the application changes.
The approach has not been further used to process NMR logging data with more complex situation .
Signal-to-noise ratio (SNR) of NMR logging is constrained by formation porosity, magnetic field strength, and instrument movement.
Some limitations:
Need to develop more comprehensive and adaptable deep learning methods that can be used in different formations and actual logging data.
Actual NMR logging echo signal
Background
What did we learn from previous work?

## Slide 8
Background
Methodology
A Lightweight Multiscale Neural Network (LMsNN) for
the Inversion of Relaxation Spectra
Experiment
Validation of Synthetic Data
  Application of NMR Rock Core Analysis
Processing with NMR Logging Data
Discussion and Further Work
Outline

## Slide 9
A lightweight multiscale neural network for inverting relaxation spectra.
Non-negative constraint on the signal is achieved by the ReLU activation function.
Convolution kernel with two sizes is used to extract multiscale features of the signal.
Softplus activation function is used to add non-negative constraints to the inverted T2 spectrum.
Adding constraints to the short relaxation components to reduce artefacts.
ReLU
Smooth constrains
Methodology
New Method: Lightweight Multiscale Neural Network (LMsNN)
Inversion:

## Slide 10
T2 spectrum acquired from the inversion part is brought into the CPMG multi-exponential decay equation to calculate a noiseless echo signal.
Forwarding
ReLU
A lightweight multiscale neural network for inverting relaxation spectra.
Smooth constrains
Methodology
New Method: Lightweight Multiscale Neural Network (LMsNN)

## Slide 11
The absolute error between the input and output echo signals.
Second-paradigm number of the inversion spectrum to introduce a smoothing constraint on the relaxation spectrum.
Loss function
ReLU
A lightweight multiscale neural network for inverting relaxation spectra.
Smooth constrains
Methodology
New Method: Lightweight Multiscale Neural Network (LMsNN)

## Slide 12
ReLU
A lightweight multiscale neural network for inverting relaxation spectra.
Smooth constrains
CPMG decay equation
Reconstruction of the echo signal
Secondary task
Constrains
Improve smoothness and accuracy of T2 spectrum
Smooth, Non-negative of Signals and spectra, Artefacts
Deep neural networks are used as as optimisers to solve this highly non-linear and underdetermined optimisation problem.
Methodology
New Method: Lightweight Multiscale Neural Network (LMsNN)

## Slide 13
Background
Methodology
A Lightweight Multiscale Neural Network (LMsNN) for
the Inversion of Relaxation Spectra
Applications
1.Validation of Synthetic Data
  2.Application of NMR Rock Core Analysis
3.Processing with NMR Logging Data
Discussion and Further Work
Outline

## Slide 14
The numerical synthetic T2 distribution models containing different ratios of BW and MO. And decay signals with different SNR corresponding to the distribution models (SNR=10, 20, 40, 80).
Established bimodal relaxation spectra for two fluid components.
Bound water (10 ms) and movable oil (150 ms) in rock pores with proportions of 3:2 and 2:3.
Simulated pulse sequence parameters, including echo spacing, number of echoes.
Calculated noiseless echo by CPMG pulse sequence response equation.
Echo signals with different SNRs are obtained by adding different levels of Gaussian noise.
Modelling two T2 distributions
Applications
1. Validation of Synthetic Data

## Slide 15
T2 spectra inverted by using BRD, SVD, and LMsNN methods based on model 1 and model 2 at different SNRs. (a) SNR = 10; (b) SNR = 20; (c) SNR = 40; (d) SNR = 80.
T2 Model 1
T2 Model 2
SNR = 10
SNR = 20
SNR = 10
SNR = 20
SNR = 40
SNR = 80
SNR = 40
SNR = 80
Applications

## Slide 16
100 random simulations and inverse by BRD, SVD, and LMsNN methods at different SNRs.
Histogram of RMSE probability statistics for two models. (a)-(d) is the result of model 1 with SNR 10, 20, 40 and 80, (e)-(h) is the result of model 2.
T2 Model 1
T2 Model 2
SNR = 10
SNR = 20
SNR = 10
SNR = 20
SNR = 40
SNR = 80
SNR = 40
SNR = 80
Applications

## Slide 17
Inversion results of four rock cores by using BRD, SVD, and LMsNN methods.
Cores |  | Scan number | SNR | Composition | Permeability
Synthetic | Core 1 | 4 | 20 | 10% chlorite with quartz sand | 1mD
 |  | 256 | 160 |  | 
 | Core 2 | 4 | 10 | Epoxy resin mixed with quartz sand | 10mD
 |  | 512 | 150 |  | 
 | Core 3 | 8 | 40 | 10% illite with quartz sand | 100mD
 |  | 256 | 160 |  | 
Real core | Core 4 | 128 | 80 | Shale stone | --
 |  | 512 | 180 |  | 
Description of cores and instrumental measurement parameters
LMsNN, BRD and SVD methods are used for core analysis.
T2 spectra inverted by LMsNN method shows high resolution compared to other methods.
T2 spectra inverted by LMsNN always indicates bimodal features, and better reduction of artefacts with short relaxation times.
LMsNN improves the accuracy of spectra for pore distribution indication
Core 2
Core 1
Core 3
Core 4
Applications
2. Application of NMR Rock Core Analysis

## Slide 18
The inverted T2 spectra by LMsNN exhibit a more remarkable bimodal than BRD method.
The calculated porosities from the inverted T2 spectra are agree with coring porosity.
LMsNN method can improve the resolution of the relaxation spectrum which further helps to complete the comprehensive evaluation of the reservoirs.
Porosity
Conventional Logging Technology
NMR Logging
Data SNR 5-10
BRD
LMsNN
Applications
3. Process NMR Logging Data

## Slide 19
Background
Methodology
A Lightweight Multiscale Neural Network (LMsNN) for
the Inversion of Relaxation Spectra
Experiment
Validation of Synthetic Data
  Application of NMR Rock Core Analysis
Processing with NMR Logging Data
Conclusions and Further Work
Outline

## Slide 20
A lightweight multi-scale neural network self-supervised training is proposed by introducing physical equations as constraints.
The new method is developed for better inversion of NMR signal accuracy and tested on Synthetic Data, rock cores and well logging data.
Adaptive extraction of key features in the echo signal to invert the T2 spectrum can be applied to formations and cores with different physical properties.
The new method provides a better indication of the pore distribution in the rock as well as helping to complete the reservoir interpretation.
Conclusions
Conclusions and Further Work

## Slide 21
Further Work
Denoising for NMR signals based on machine learning.
Intelligent interpretation of NMR relaxation spectra.
Providing quantitative evaluation of fluids.
Conclusions and Further Work

## Slide 22
Thanks for your attention
Questions and comments