## Slide 1: Comparative Study of Carbon Dioxide and Hydrogen Relative Permeability, Pore Occupancy, Connectivity and Ostwald Ripening in Carbonate Rocks
Presenter: Ahmed AlZaabi
Supervisors: Prof. Martin J. Blunt & Dr. Branko Bijeljic
14/01/2026

## Slide 2: Agenda
Previous Study
Research Objectives
Research method
Results and Discussion
  Relative Permeability
  Pore Occupancy
  Connectivity
  Ostwald Ripening
Conclusions
Future work

## Slide 3: Previous Study
Gas ganglia increase in size with time.
The gas ganglia are more connected with time.
Ostwald Ripening differences between gases
 | N₂
 | N₂ after 24 h
 | CO₂
 | CO₂ after 24 h
 | H₂
 | H₂ after 24 h
 | H₂ after 48 h
H₂
100 µm
CO₂
100 µm
N₂
100 µm
AlZaabi, A., Alzahrani, H. M., Alhosani, A., Bijeljic, B., & Blunt, M. J. (2025). Wettability, pore occupancy, connectivity and Ostwald ripening of nitrogen, carbon dioxide, and hydrogen in carbonate rocks: A comparative study. International Journal of Hydrogen Energy, 135, 596-608.

## Slide 4: Research Objectives
The configuration of hydrogen within the pore space has not been extensively investigated for storage applications.
Carbon dioxide in a super-critical state, have been more studied: this work provides a direct comparison of its behavior with hydrogen.
The rock sample is a reservoir carbonate, as opposed to the sandstones and/or quarry samples used in previous work.

## Slide 5: Research method
Experimental Apparatus
Xradia Versa μ-CT X-ray microscopy is used for image acquisition.
Experimental Conditions:
Pressure = 8 MPa
Temperature = 50 ◦C
Injection rate = 0.5 mL/min

## Slide 6: Research method
Fluid Injection path
Brine and gas are injected from below the sample.
Fractional flow table:
Flooding# | fw | fg
1 | 1 | 0
2 | 0.8 | 0.2
3 | 0.5 | 0.5
4 | 0.1 | 0.9
5 | 0.05 | 0.95
6 | 0 | 1
Brine injection path
Gas injection path

## Slide 7: Research method
Experimental Procedure

## Slide 8: Research method
The saturation and ganglia analysis is determined across the whole sample.
The pore occupancy, curvature analysis and wettability is measured on a sub volume.
Image Analysis
Whole Sample
Sub volume
Generated Surface
1
3
2
1 mm
8 μm

## Slide 9: Results and Discussion
Relative Permeability

## Slide 10: Results and Discussion
To analyse the pore occupancy, several sub volumes of 400×400×400 voxels (135.14×135.14×135.14 μm3) were considered.
As expected for a water-wet system, the gas phase, being non-wetting, tends to reside in the larger pores and throats.
H₂ occupies larger pores relative to CO₂.
Pore Occupancy

## Slide 11: Results and Discussion
Carbon dioxide is less connected than hydrogen.
Connectivity is quantified using Euler number.
Low Euler number implies better connected phases.
Connectivity
1 mm
CO₂
µmᶟ
0 10⁷
H₂
1 mm
Image | Normalized (1/mmᶟ)
CO₂ | 12
H₂ | 4

## Slide 12: Conclusions
To compare CO₂ and H₂ injection in a reservoir carbonate rock, three-dimensional µ-CT imaging was used.
Relative permeability: H₂ has lower relative permeability than CO₂.
Pore occupancy: H₂ bubbles occupy the larger pores as opposed to CO₂.
  Gas connectivity and Ostwald ripening: All the gases show better connectivity with time: good for retrieval, bad for sequestration.
  Implications: These results provides insight for underground H₂ storage (UHS) for clean energy storage and carbon capture and storage (CCS) projects to reduce greenhouse effect.

## Slide 13: Future analysis
Continue the analysis and investigate: wettability, ganglia analysis, capillary pressure and saturation profiles.
Analyse images that were taken almost every day up to 7 days without injection to study the effect of Ostwald ripening effect.
Analyse the results from the experiment after altering the wettability.

## Slide 14: Thank you
Comparative Study of Carbon Dioxide and Hydrogen Relative Permeability, Pore Occupancy, Connectivity and Ostwald Ripening in Carbonate Rocks
14/01/2026

## Slide 15: References
Alhammadi, A. M., AlRatrout, A., Singh, K., Bijeljic, B., & Blunt, M. J. (2017). In situ characterization of mixed-wettability in a reservoir rock at subsurface conditions. Scientific Reports, 7(1), 10753.
Alhosani, A., Bijeljic, B., & Blunt, M. J. (2021a). Pore-scale imaging and analysis of wettability order, trapping and displacement in three-phase flow in porous media with various wettabilities. Transport in Porous Media, 140(1), 59-84.
Alhosani, A., Lin, Q., Scanziani, A., Andrews, E., Zhang, K., Bijeljic, B., & Blunt, M. J. (2021b). Pore-scale characterization of carbon dioxide storage at immiscible and near-miscible conditions in altered-wettability reservoir rocks. International Journal of Greenhouse Gas Control, 105, 103232.
Alhosani, A., Scanziani, A., Lin, Q., Foroughi, S., Alhammadi, A. M., Blunt, M. J., & Bijeljic, B. (2020). Dynamics of water injection in an oil-wet reservoir rock at subsurface conditions: Invasion patterns and pore-filling events. Physical Review E, 102(2), 023110.
Blunt, M. J. (2022). Ostwald ripening and gravitational equilibrium: Implications for long-term subsurface gas storage. Physical Review E, 106(4), 045103.
de Chalendar, J. A., Garing, C., & Benson, S. M. (2018). Pore-scale modelling of Ostwald ripening. Journal of Fluid Mechanics, 835, 363-392.
Foroughi, S., Bijeljic, B., & Blunt, M. J. (2021). Pore-by-pore modelling, validation and prediction of waterflooding in oil-wet rocks using dynamic synchrotron data. Transport in Porous Media, 138(2), 285-308.
Foroughi, S., Bijeljic, B., Lin, Q., Raeini, A. Q., & Blunt, M. J. (2020). Pore-by-pore modeling, analysis, and prediction of two-phase flow in mixed-wet rocks. Physical Review E, 102(2), 023302.
Goodarzi, S., Zhang, Y., Foroughi, S., Bijeljic, B., & Blunt, M. J. (2024). Trapping, hysteresis and Ostwald ripening in hydrogen storage: A pore-scale imaging study. International Journal of Hydrogen Energy, 56, 1139-1151.
Hematpur, H., Abdollahi, R., Rostami, S., Haghighi, M., & Blunt, M. J. (2023). Review of underground hydrogen storage: Concepts and challenges. Advances in Geo-Energy Research, 7(2), 111-131.
Iglauer, S., Ali, M., & Keshavarz, A. (2021). Hydrogen wettability of sandstone reservoirs: implications for hydrogen geo‐storage. Geophysical Research Letters, 48(3), e2020GL090814.

## Slide 16: Acknowledgment
Supervisors
Prof. Martin J Blunt
Dr. Branko Bijeljic
Dr. Shehadeh Masalmeh
Experiment and analysis
Dr. Rukuan Chai
Qianqian Ma
Dr. Hussain Alzahrani
Waleed Dokhon
Anfal Al Zarafi
Dr. Vinchenzo Cunsolo
Funding
Abu Dhabi National Oil Company (ADNOC)