## Slide 1: Field-scale Analysis of Hydrogen Storage Incorporating Pore-scale Hysteresis Models
Ibrahim Alobaidan – PhD Student
Supervisors: Prof Martin Blunt and Dr Branko Bijeljic
14/01/2026

## Slide 2: Key Insights from Pore-Scale Studies
 | N₂
 | N₂ after 24 h
 | CO₂
 | CO₂ after 24 h
 | H₂
 | H₂ after 24 h
 | H₂ after 48 h
H₂
100 µm
CO₂
100 µm
N₂
100 µm
Ostwald Ripening in different gases (AlZaabi et al., 2025)
Image | Normalized (1/mm3)
N₂ | 201
N₂ after 24 h | 89
CO₂ | 12
CO₂ after 24 h | 4
H₂ | 4
H₂ after 24 h | 3
H₂ after 48 h | 0
Euler Number
* Low Euler number implies better connected phases
Over time, gas redistributes within the pore space without changing overall volume, a process known as Ostwald ripening. (Goodarzi et al., 2024)
This redistribution improves connectivity and enables hydrogen withdrawal through continuous pathways. (Goodarzi et al., 2024)
Repeated drainage and imbibition cycles lower residual saturations. (Goodarzi et al., 2024)
Pressure decline, gas expansion, and exsolution can remobilize trapped hydrogen ganglia (Dokhon et al., 2024).
Ignoring gas remobilisation effects leads to an overestimation of trapping by 20–25% (Adebimpe et al., 2024).
Traditional trapping and hysteresis models do not capture the trends observed in pore-scale measurements. (Goodarzi et al., 2024)

## Slide 3: Research Objective
Incorporating pore-scale data from in-house experiments and modelling outputs into field-scale simulations to:
Investigate recovery mechanisms in underground hydrogen storage (UHS) under various simulation scenarios.
Evaluate the applicability of traditional relative permeability trapping and hysteresis models for UHS.
Implement a flexible hysteresis module into research reservoir simulators (OPM Flow and QASR) to account for pore-scale processes associated with UHS.
Study the effects of gas remobilisation due to pressure-driven hydrogen expansion and Ostwald ripening on recovery.

## Slide 4: Pore-to-field Scale Research Workflow
Pore-Scale Imaging and Measurements
Flexible hysteresis module
Research Simulators
(OPM Flow & QASR)
Reservoir Simulator
(CMG)
Include gas remobilization
Hydrogen expansion
Ostwald Ripening
Implementing the Spiteri model
Sensitivity Analysis
(OPM Hysteresis library)
Validation
Input data
- 3D geological structure
- Porosity, ϕ
- Permeability, k
- Phase behavior data
- Relative permeability, kr
- Capillary pressure, Pc
- Gas saturation, Sg
Traditional modelling approach
Benchmarking
PART 1
PART 2
Field-scale
analysis
PART 3
Wettability
Effects
Pore-scale modelling
Calibration of Spiteri parameters
𝛼, 𝛽, 𝛾
^ OPM Flow is an open-source reservoir simulator, developed under the Open Porous Media project (OPM)
^ QASR is a reservoir simulator developed by Dr Ahmad Abushaikha – former PhD student in our research group, now at Hamad Bin Khalifa University, Qatar
Scan to view full paper

## Slide 5: Traditional Trapping & Hysteresis Models
Carlson Model (1981)
Flowing gas saturation,
Gas relative permeability, :
Land’s Trapping Model (1968)
Land’s parameter, :
Trapped gas saturation, :
Killough Model (1976)
Normalised gas saturation, :
Gas relative permeability, :
)
Advantages
Standard in most reservoir simulators
Require minimal pore-scale input data
Historically validated and widely used
Limitations
Reliable mainly for strongly water-wet rocks
Cannot capture wettability variation or key pore-scale trapping mechanisms
+
-
Notes: Now let’s look at traditional trapping and hysteresis models.
The most common are the Land, Killough, and Carlson models.
The Land model links initial gas saturation to trapped gas saturation, as shown in this plot, using a parameter derived from relative permeability data — 𝑺_𝒈𝒎𝒂𝒙and 𝑺_𝒈𝒕𝒎𝒂𝒙.
The Killough and Carlson models then use Land’s trapping function to generate scanning curves, based on the maximum gas saturation in each simulator cell. The red lines here show scanning curves generated with these models.
These models are standard in most reservoir simulators, require minimal pore-scale input, and have been historically validated.
But their limitation is clear: they are reliable mainly for strongly water-wet rocks, and they do not capture wettability variation or the pore-scale trapping mechanisms that are critical in hydrogen storage.

## Slide 6: Reservoir Cross-Sectional Comparison of Gas Saturation
No hysteresis
Carlson hysteresis
Killough hysteresis
Sg

## Slide 7: Flexible Trapping & Hysteresis Models
Spiteri et al. Model (2005)
Trapped gas saturation, :
: slope of the initial residual curve
: curvature of the initial residual curve
: flow parameter, dependent on rock type and wettability
Flowing gas saturation,
Gas relative permeability, :
Advantages
Captures wettability variation
Flexible to incorporate other pore-scale trapping mechanisms
Limitations
Requires extensive calibration data
Never implemented in reservoir simulators
Highly non-linear and computationally demanding
+
-

## Slide 8: Implementing the Spiteri Model into OPM Flow Reservoir Simulator
Spiteri et al. Model (2005)
Trapped gas saturation, :
: slope of the initial residual curve
: curvature of the initial residual curve
: flow parameter, dependent on rock type and wettability
Flowing gas saturation, (numerically stable form for simulators)
Gas relative permeability, :
1
1
2
2
3
3

## Slide 9: Pore-Scale Modelling for Trapping and Relative Permeability
CT Image
^ sample scanned dry using Xradia Versa 500 micro-CT scanner at iRock Technologies
Cooperative pore-filling
Blunt model [1998]
are arbitrary numbers and are random numbers between 0 and 1
Contact angles have been assigned throughout the network randomly within ±20° of the average value
A uniform distribution has been used
Rock type | Berea Sandstone
Voxel Dimensions | 1024 × 1024 × 1024
Voxel Size | 2.7745 μm
Physical Size | ~2.84 mm × 2.84 mm × 2.84 mm
Voxel Count | 1,073,741,824 (1.07B)
Porosity | 20.18%
Permeability | 985.17 mD
Relationship between receding and advancing contact angles on a rough surface, as a function of intrinsic contact angle measured at rest on a smooth surface (Morrow 1975).

## Slide 10: Calibration of Spiteri Parameters: 𝛼, 𝛽 & 𝛾
Strongly Water-Wet
Mixed-Wet

## Slide 11: Numerical Simulation
Property​ | Unit​ | Value
No. of active grid cells​ | ​ | 47,547
Discretization​ | m​ | 60 × 60 × 1 ​
Depth to surface​ | m​ | 840​
Thickness​, | m​ | 15​
Avg. porosity, |  | 0.20
Avg. horizontal permeability, | mD | 200
Pressure​, | MPa​ | 9​
Temperature​, | C​ | 40​
Rock compressibility​, | 1/kPa​ | 7.04 × 10-7​
Vertical anisotropy - | ​ | 0.3​
Water compressibility​, | 1/kPa​ | 4.07×10-7 ​
Water density​, | kg/m3​ | 992.22​
Water molar mass, | kg/mol | 0.018
Water viscosity​, | mPa.s | 0.653​
Property​ | Unit​ | Value
No. of active grid cells​ | ​ | 47,547
Discretization​ | m​ | 60 × 60 × 1 ​
Depth to surface​ | m​ | 840​
 | m​ | 15​
 |  | 0.20
 | mD | 200
 | MPa​ | 9​
 | C​ | 40​
 | 1/kPa​ | 7.04 × 10-7​
 | ​ | 0.3​
 | 1/kPa​ | 4.07×10-7 ​
 | kg/m3​ | 992.22​
 | kg/mol | 0.018
 | mPa.s | 0.653​
Parameter | Unit​ | Value
Working gas (WG)​ | ​ | H2​
Injection & Production rate​ | sm3/day​ | 200,000​
Production well diameter​ | m​ | 0.1524​
Min bottom-hole pressure​ | MPa​ | 5​
Max bottom-hole pressure​ | MPa​ | 16
Inje/prod period per cycle​ | Months​ | 6 ​
 | No Hysteresis | Killough |  | Carlson |  | Spiteri | 
Case ID | A | B1 | B2 | C1 | C2 | D1 | D2
Wettability (°) | — | 20 | 100 | 20 | 100 | 20 | 100
C | — | 1.4016 | 18.6763 | 1.4016 | 18.6763 | — | —
 | — | — | — | — | — | 0.8500 | 0.8184
 | — | — | — | — | — | 0.4633 | 0.9962
 | — | — | — | — | — | -0.1000 | 2.30
Operational parameters
Aquifer model parameters
2D porosity and permeability maps of the aquifer model
Summary of simulation scenarios
Simulator | ​OPM Flow
Flow model | ​Black-oil
Flow regime | ​Gas-water
Hysteresis | Modified OPM hysteresis library​
Simulation settings

## Slide 12: Krg vs Sg: Location 1 - Cell (32, 53, 1)
● NO HYSTERESIS | ● KILLOUGH | ● CARLSON | ● SPITERI
Water
wet
Mixed
wet

## Slide 13: Krg vs Sg: Location 2 - Cell (45, 65, 1)
● NO HYSTERESIS | ● KILLOUGH | ● CARLSON | ● SPITERI
Water
wet
Mixed
wet

## Slide 14: Effect of Hysteresis and Wettability on Rate, Pressure & H2 Recovery
Water
wet
Mixed
wet

## Slide 15: Conclusion and Future Work
Under strongly water-wet conditions, all hysteresis models produced comparable recovery and pressure responses.
Under mixed-wet conditions, Carlson and Killough models systematically overestimated gas recovery.
Adjusting Land’s trapping parameter is insufficient to capture non-monotonic pore-scale trapping.
Apply the proposed pore-to-field scale modelling approach to in-house sandstone and carbonate samples
Validate the approach against multiphase flow characteristics measured under displacement and during both pressure increase and decline.
Apply the new proposed approach to address conditions beyond traditional oilfield flow measurements, explicitly accounting for gas remobilisation driven by hydrogen expansion and Ostwald ripening

## Slide 16: References
Alobaidan, I. A., Bijeljic, B., & Blunt, M. J. (2025). Drive mechanisms and hydrogen recovery in underground storage. Int. J. Hydrogen Energy, 146, 149891. https://doi.org/10.1016/j.ijhydene.2025.06.081
Goodarzi, S., Zhang, Y., Foroughi, S., Bijeljic, B., & Blunt, M. J. (2024). Trapping, hysteresis and Ostwald ripening in hydrogen storage. Int. J. Hydrogen Energy, 56(2), 1139–1151. https://doi.org/10.1016/j.ijhydene.2023.12.029
Dokhon, W., Goodarzi, S., Alzahrani, H. M., Blunt, M. J., & Bijeljic, B. (2024). Pressure decline and gas expansion in underground H₂ storage. Int. J. Hydrogen Energy, 86, 261–274. https://doi.org/10.1016/j.ijhydene.2024.08.139
AlZaabi, A., Alzahrani, H. M., Alhosani, A., Bijeljic, B., & Blunt, M. J. (2025). Wettability, pore occupancy and Ostwald ripening in N₂, CO₂ and H₂. Int. J. Hydrogen Energy, 135(1), 596–608. https://doi.org/10.1016/j.ijhydene.2025.04.399
Adebimpe, A. I., Foroughi, S., Bijeljic, B., & Blunt, M. J. (2024). Percolation without trapping: Ostwald ripening in porous media. Phys. Rev. E, 110(3), 035105. https://doi.org/10.1103/PhysRevE.110.035105

## Slide 17: Acknowledgements
Supervisors
Prof Martin Blunt
Dr Branko Bijeljic
External Collaborator
Dr Ahmad Abushaikha
Funding
Saudi Aramco
Pore-scale Imaging and Modelling
Dr Sajjad Foroughi
Dr Sepideh Goodarzi
Abdulaziz Alsaleh
Ademola Adebimpe
Ahmad AlZaabi
Waleed Dokhon

## Slide 18: Thank you